## Slide 1
CE222 · COMPUTER ORGANIZATION GIK INSTITUTE · 2026
VERA-16
A 2-Address 16-bit Processor
Architecting Efficiency with General-Purpose Register Files
Usman Azhar
ID: 2024653
Reyan Kashif
ID: 2024538
Muhammad Saim
ID: 2024453

## Slide 2
PROBLEM & MOTIVATION: WHY VERA-16?
THE ACCUMULATOR BOTTLENECK
01
Single accumulator (AC) for all arithmetic operations.
02
16 bits Instruction but 1 address
03
Results must return to memory before reuse.
04
Limited instruction types (8) and addressing modes (2).
→
THE VERA-16 SOLUTION
01
8 general-purpose 16-bit registers (R0–R7).
02
16-bits, with 2-address format: any register as source or destination.
03
Register access eliminate memory use between code execution
04
33 instructions across 5-bit opcode space.

## Slide 3
DESIGN AT A GLANCE: ARCHITECTURE OVERVIEW
WORD SIZE
16-BIT
Unified data and instruction width
MEMORY (RAM)
4096×16
Addressable memory space
REGISTER FILE
8 REGS
R0–R7 General-Purpose Registers
INSTRUCTION SET
33 OPS
Comprehensive functional coverage
OPCODE SPACE
5-BIT
Up to 32 instruction slots
ADDRESSING
4 MODES
Reg, Imm, Direct, Reg-Indirect
INSTRUCTION WORD: OPCODE(5) | MODE(2) | DST(3) | SRC(6) = 16 BITS

## Slide 4
16-BIT INSTRUCTION WORD FORMAT
OPCODE
15 : 11
MODE
10 : 9
DST
8 : 6
SRC
5 : 0
5 bits → 32 instruction slots
4 addressing modes
Destination Reg (R0–R7)
Register, value, or address
WORKED EXAMPLE: ADD R2, R5
FIELD
VALUE
BINARY REPRESENTATION
OPCODE
ADD (0)
00000
MODE
Reg-to-Reg (0)
00
DST
R2
010
SRC
R5
000101
FULL INSTRUCTION: 00000 00 010 000101

## Slide 5
33 INSTRUCTIONS: FUNCTIONAL CATEGORIES
ARITHMETIC
ADD SUB MUL INC DEC CMP
LOGIC
AND OR XOR NOT CMR
SHIFT
SHL SHR
DATA TRANSFER
MOV LDI LDM STM
CONTROL
JMP JZ JNZ HLT
I/O & INTERRUPT
INP OUT SKI SKO ION IOF
TECHNICAL NOTE: Register-reference group (opcode 11110) uses one-hot bit encoding for 7 sub-operations.

## Slide 6
INSIDE THE ALU: ARITHMETIC LOGIC UNIT
RIPPLE-CARRY ADDER
16-bit Architecture. Handles ADD, SUB, INC, and DEC operations. Utilizes a MUX-selected Y-input for versatile arithmetic processing.
LOGIC UNIT
16 One-bit Slices. Performs AND, OR, XOR, and NOT operations. Each slice features a 4×1 MUX for rapid logical computation.
BARREL SHIFTER
Dynamic Shifting. Shifts left or right by n positions (n from IR[3:0]). Captures the shifted-out bit in the Carry flag.
ARRAY MULTIPLIER
Hardware Native. 16 rows of AND gates + 15 adders. Produces a 32-bit product; the lower 16 bits are stored in the DST register.
OUTPUT SELECTION: A 4×1 MUX (controlled by S3, S2) selects the sub-unit result for the register file.

## Slide 7
FETCH-DECODE-EXECUTE: CONTROL UNIT CYCLE
PHASE 01
FETCH
AR ← PC
Address of next instruction moved to Address Register.
IR ← M[AR]
Instruction fetched from memory into Instruction Register.
PC ← PC + 1
Program Counter incremented for the next cycle.
PHASE 02
DECODE
IR[15:11] → DEC
5-bit Opcode sent to the instruction decoder.
IR[10:9] → MODE
2-bit Addressing Mode identified.
IR[8:0] → REGS
Destination (3-bit) and Source (6-bit) fields extracted.
PHASE 03
EXECUTE
CTRL GEN
Control Unit generates timing signals (T0-T7).
ALU OP
Arithmetic or Logic operation performed by ALU.
REG WRITE
Result stored back into the Destination Register.

## Slide 8
I/O OPERATIONS & INTERRUPT MECHANISM
INPUT / OUTPUT
INP (Input)
Data from Input Device → INPR → AC
OUT (Output)
AC → OUTR → Output Device
SKI (Skip Input Flag)
If FGI = 1, increment PC (Skip next)
SKO (Skip Output Flag)
If FGO = 1, increment PC (Skip next)
INTERRUPT HANDLING
TRIGGER: IEN=1 AND (FGI=1 OR FGO=1) → R ← 1
PHASE
MICRO-OPERATIONS
DESCRIPTION
RT0
AR ← 0, TR ← PC
Save return address in TR
RT1
M[AR] ← TR, PC ← 0
Store PC at memory address 0
RT2
PC ← 1, IEN ← 0, R ← 0
Jump to ISR (Addr 1), clear flags
Note: Interrupts are processed only after a full Fetch-Decode-Execute cycle is completed.

## Slide 9
VERA-16 VS. MANO MACHINE: ARCHITECTURAL EVOLUTION
FEATURE
MANO MACHINE
VERA-16 PROCESSOR
Architecture
1-address (Accumulator)
2-address (Register File)
Opcode Bits
3 bits → 8 instructions slots
5 bits → 32 instruction slots
Registers
1 (AC only)
8 GP registers (R0–R7)
Addressing
2 (Direct, Indirect)
4 (Reg, Imm, Direct, Reg-Indirect)
Hardware Multiply
Software loop required
Array Multiplier (Native)
ALU Operations
ADD, AND, Complement, Shift
ADD, SUB, MUL, AND, OR, XOR, NOT, Shifts
Sequence Counter
4-bit (T0–T15)
3-bit (T0–T7) — Reduced Hardware

## Slide 10
CONCLUSION & PRESENTATION SPLIT
KEY TAKEAWAYS
Efficiency: VERA-16 eliminates the accumulator bottleneck with 8 general-purpose registers.
Versatility: 2-address format and 5-bit opcode enable 33 instructions and 4 addressing modes.
Performance: Hardware array multiplier and barrel shifter provide superior ALU capability.
Simplicity: 3-bit sequence counter reduces control unit hardware complexity.
Validation: Fully functional software simulator validates every instruction in real-time.
TEAM
Usman Azhar
ID: 2024653
Reyan Kashif
ID: 2024538
Muhammad Saim
ID: 2024453
VERA-16 · CE222 · GIK INSTITUTE · APRIL 2026